## Slide 1: Wearing Predictive System
Dalla Longa Emanuele
Milani Federico
Urzino Davide
Project 8

## Slide 2: Project target
We want to obtain a system able to detect faults on an industrial motor using the BlueCoin hearing and motion sensing platform by ST Microelectronics
Industrial motor
BlueCoin from ST

## Slide 3: Why BlueCoin
Little platform with the advantage to be easily located directly on the motor
It includes some useful sensors (magnetometer, mems microphones array, pressure sensor, gyroscope) and Bluetooth communication
Powerful enough to execute the tasks to identify a faulty motor
Completely programmable to use only the needed sensors in order to increase energy efficiency
Lots of compatibility with other ST Microelectronics boards and expansion devices

## Slide 4: The system must
capture the properties of a correctly working motor
monitor the motor in order to figure out if one or more of these properties are faulty, producing an alarm when something is detected

## Slide 5: The system should
reduce as much as possible the amount of work on the BlueCoin, in order to increase its battery duration
be adaptable to different motors autonomously

## Slide 6: Capturing the motor properties
In order to accomplish this, the task will be split into two subtasks:
Data acquisition: the BlueCoin will be used to sense data from the motor in order to catch as much of its dynamics as possible
Model identification: the data collected will be fed to a model identification algorithm that will try to detect the model describing the motor

## Slide 7: Detecting the motor faults
Once the motor model has been detected, the BlueCoin will keep sensing data from the motor and deliver them to an external data processing unit that will:
Check if the received data fits the model
Launch an alarm if they don’t

## Slide 8: Being energy efficient
The BlueCoin activity will follow a duty cycle like this

## Slide 9: Being autonomous
The system should not work only with a single motor since each one has a different dynamic based on it’s usage.
That’s why the system should, on it’s first usage on a new motor, perform a preliminary calibration phase in order to adapt the model to the singular characteristics of the current motor.

## Slide 10: Overall work cycle
Data checking
Positive/Negative Output
Data sensing
Blue coin installation and connection with the data processing unit
Model identification
Data sensing

## Slide 11: System topology
Motor 1
Motor N
BlueCoin1
BlueCoin N
Data Processing Unit
Data1
Data N
Web Server
Web Page with monitoring results (ok/ko)
Motor power supply controller that turns off a motor in case of faults
Power supply
Target
Possible system improvement