## Slide 1: Wearing Predictive System
Dalla Longa Emanuele
Milani Federico
Urzino Davide
Project 8

## Slide 2: Project target
Detect faults on an industrial electric motor

## Slide 3: Platform
We used STM32 BlueCoin as our prototype board
Little platform which can be easily bolt on the motor without the need of modifications
Wide sensor capabilities (magnetometer, gyroscope, accelerometer)
SD card interface
Can be used for future iterations, which may need to exploit features like Bluetooth transmission, low power mode…

## Slide 4: Workflow
We have three main tasks to tackle:
Data acquisition: we sense data using the BlueCoin board, and then collect them
  The prototype we have developed in this iteration records data on a testbed, in a clean environment, free of interferences, at a given regime.
  Data are logged on a SD card

## Slide 5: Workflow
Model identification: we feed these data into a modeling algorithm, which estimates the system characteristics:
  We have implemented an advanced modeling algorithm which estimates an NAR(MA) model for each sensor axis, on a clean set of data

## Slide 6: Workflow
Fault detection: we check the prediction performance of our model on the newly sensed data
  If the performance of the prediction is worse than a certain threshold, we will know that the model has changed and the test will fail
  The frequency of these checks will be proportional to the load applied
  These checks will be operated more often in the first period of the motor’s life and near its expected end

## Slide 7: Test workflow
Motor N
Motor 2
Motor 1
BlueCoin
User interface
Data Processing Unit
SD

## Slide 8: Experiments
We performed an experiment to verify the capabilities of the developed tools, using a fan rotating at the same speed as the motor
  Data sensing on a working fan
  Data sensing on a modified fan
    Eccentrical load
    Magnetic field
  Model identification on the working fan data and performance verification on disturbed data

## Slide 9: Experiments
We used two fans with a different diameter
The BlueCoin has been screwed on a plastic cradle taped to each fan

## Slide 10: Experiments: modified conditions
We interfered with the rotation with a plastic rod
We added some tape on a blade of the fan
We taped a magnet on a blade of the fan
We broke one of the fan supports

## Slide 11: Acquisition demo

## Slide 12: Results: testing on good data

## Slide 13: Results: plastic rod

## Slide 14: Results: taped blade

## Slide 15: Results: magnet taped on blade

## Slide 16: Future possibilities
Future iterations could:
Identify fault types by modeling their signatures on faulty motors
Collect data online This feature will need to handle further concerns, like:
  Energy efficiency (harvesting?)
  Drift (adaptivity)