## Slide 1: Wearing Predictive System
Dalla Longa Emanuele
Milani Federico
Urzino Davide
Project 8

## Slide 2: Project target
We want to obtain a system able to detect faults on an industrial motor using the BlueCoin hearing and motion sensing platform by ST Microelectronics
Industrial motor
BlueCoin from ST

## Slide 3: Why BlueCoin
Little platform with the advantage to be easily located directly on the motor
It includes some useful sensors (magnetometer, gyroscope, accelerometer) and the possibility to log data on an SD card
Powerful enough to execute the needed tasks
Completely programmable to use only the needed sensors in order to increase energy efficiency

## Slide 4: The system must
capture the properties of a correctly working motor
check the motor data in order to figure out if one or more of its properties are faulty, showing that something is wrong

## Slide 5: The system should
reduce as much as possible the amount of work on the BlueCoin, in order to avoid energy efficiency issues
be adaptable to different motors and environments

## Slide 6: 1) Capturing the motor properties
In order to accomplish this, the task will be split into two subtasks:
Data acquisition: the BlueCoin will be used to sense and save data the to an SD card from the motor in order to catch as much of its dynamics as possible
Model identification: the data collected will be fed to a model identification algorithm that will try to detect the model describing the motor

## Slide 7: 2) Detecting the motor faults
Once the motor model has been detected, the BlueCoin will be used to read and save data from the motor with a frequency depending on its usage and they will be used by an external data processing unit that will:
Check if the data fits the model
Launch an alarm if they don’t

## Slide 8: 3) Avoid energy issues
The BlueCoin will be used only to gather data and an external tool will be used to perform the data analysis task.

## Slide 9: 4) Being autonomous
The system should not work only with a single motor since each one has a different dynamic based on it’s usage.
On the first usage on a new motor, the motor is considered in good conditions and some data must be collected to perform a preliminary calibration phase in order to adapt the model to the singular characteristics of the current motor.
This procedure allows to have a “personalized” model for each motor.

## Slide 10: Overall work cycle
Blue coin installation on motor
Model identification
Data sensing
Blue coin installation on motor
Data checking
Data sensing
Positive/Negative Output
First usage on a motor
Next usages on the same motor

## Slide 11: System topology
Motor N
Motor 1
BlueCoin
Data Processing Unit
Display for result monitoring
Target
SD

## Slide 12: What has been achieved
A simpler board has been used as a prototype to test the sensors

## Slide 13
The code for sensing developed on the prototype has been migrated on the BlueCoin with the addition of the SD-card logging

## Slide 14
An experiment has been performed:
  Data sensing on a stable plain
  Data sensing including disturbances on the plain
  Model identification on the stable plain data and comparison with disturbed data

## Slide 15: Stable plain data 1

## Slide 16: Stable plain data 2

## Slide 17: Disturbed plain data

## Slide 18: Model identification and data checking results
Stable plain 1
Stable plain 2
Disturbed plain