## Slide 1: Wearing Predictive System
Dalla Longa Emanuele
Milani Federico
Urzino Davide
Project 8

## Slide 2: Project target
Detect faults on an industrial electric motor

## Slide 3: Platform
We used STM32 BlueCoin as our prototype board
Little platform which can be easily bolt on the motor without the need of modifications
Wide sensor capabilities (magnetometer, gyroscope, accelerometer)
SD card interface
Can be used for future iterations, which may need to exploit features like Bluetooth transmission, low power mode…

## Slide 4: Capturing the motor properties
We have three main tasks to tackle:
Data acquisition: we sense data using the BlueCoin board, and then collect them
  The prototype we have developed in this iteration records data on a testbed, in a clean environment, free of interferences, at a given regime.
  Data are logged on a SD card

## Slide 5: Capturing the motor properties
Model identification: we feed these data into a modeling algorithm, which estimates the system characteristics:
  We have implemented an advanced modeling algorithm which estimates an AR(MA) model for each sensor axis, on a clean set of data

## Slide 6: Monitoring the motor state
Fault detection: we check the prediction performance of our model on the newly sensed data
  If the performance of the prediction is worse than a certain threshold, we will know that the model has changed and the test will fail
  The frequency of these checks will be proportional to the load applied
  These checks will be operated more often in the first period of the motor’s life and near its expected end

## Slide 7: Overall work cycle
Blue coin installation on motor
Model identification
Data sensing
Blue coin installation on motor
Data checking
Data sensing
Test result
First acquisition: Model Identification
Next acquisitions: fault detection

## Slide 8: Test workflow
Motor N
Motor 2
Motor 1
BlueCoin
User interface
Data Processing Unit
SD

## Slide 9: Experiments
We performed an experiment to verify the capabilities of the developed tools:
  Data sensing on a working fan
  Data sensing with modifications to a blade of the fan
    Eccentrical load
    Magnetic field
  Model identification on the working fan data and performance verification on disturbed data

## Slide 10: Experiments: Sampling frequency
The working regime of the fans we are working with is between 600-3000 rpm
  This is coherent with industrial motors
  We assumed that this is the only harmonic we are interested in
    We applied a low-pass antialiasing FIR filter
  We chose a sampling frequency 10 times greater than that
    We don’t have memory constraints

## Slide 11: Experiments
We used two fans with a different diameter
The BlueCoin has been screwed on a plastic cradle taped to the fan
We powered the fans using an ATX power supply

## Slide 12: Experiments: modified conditions
We interfered with the rotation with a plastic rod
We added some tape on a blade of the fan
We taped a magnet on a blade of the fan
We broke one of the fan supports

## Slide 13: Results: testing on good data

## Slide 14: Results: plastic rod

## Slide 15: Results: taped blade

## Slide 16: Results: magnet taped on blade

## Slide 17: Future possibilities
Future iterations could provide online data sensing and collection. This configuration will need to handle further concerns, like:
  Online data collection
  Energy efficiency (harvesting?)
  Drift (adaptivity)